## Slide 1: Antenna Alternatives
Nick Hall-Patch
IRCA-NRC-WTFDA-DecalcoMania Convention 2016

## Slide 2: Antenna Alternatives
An alternative to THE antenna:
The Double Kaz (DKaz)
good directivity within a limited space

## Slide 3: Antenna Alternatives
So, what’s the alternative?

## Slide 4: Antenna Alternatives
What might one need in an antenna?
  Ability to pick up signals
  Directionality?
  Wide frequency coverage?

## Slide 5: Antenna Alternatives
Limitations to one’s antenna choices
      small footprint?
      low cost?
      avoidance of local noise problems?
      strong local signals?
      will this be a temporary or stealth antenna?

## Slide 6
  Lots of receiving antennas from which to choose
        Omnidirectional
        Bidirectional
        Unidirectional
Antenna Alternatives

## Slide 7: Antenna Alternatives -- omnidirectional
Omnidirectional antennas
-----tend to be a vertical antenna or a variation
vertical wire (transformer coupled )
  random wire
active whip

## Slide 8: Antenna Alternatives -- omnidirectional
Vertical antennas
-----not exactly omnidirectional

## Slide 9: Vertical antennas
Antenna Alternatives -- unidirectional

## Slide 10: Antenna Alternatives -- omnidirectional
Vertical antennas
----transformer coupling to feedline is best, 15 to 30’
advantages:
small footprint
inexpensive and fairly easy to build
broadband
can be quite sensitive
resistant to feeder conducted electrical noise
disadvantages:
better sensitivity requires more vertical height
a better quality ground delivers better signal

## Slide 11: Active whip
Antenna Alternatives -- unidirectional

## Slide 12: Antenna Alternatives -- omnidirectional
Active whip
--usually a small antenna element <4’ long, plus amplifier
advantages:
small footprint
does not need a ground connection for operation
broadband
sensitive
can be homebrewed
disadvantages:
requires placement away from nearby objects
generally sensitive to local electrical noise
trade off between sensitivity and strong signal handling
can be costly

## Slide 13: Antenna Alternatives -- bidirectional
Bidirectional antennas
  For the home user, these are likely to be loop antennas
used for nulling interfering stations, but also for direction finding

## Slide 14: Bidirectional antennas
  tuned loop antennas
  broadband loop antennas

## Slide 15: tuned loop antennas
ferrite-core
air-core

## Slide 16: Antenna Alternatives -- bidirectional
tuned loop
advantages:
  small footprint
  small enough to be used indoors, particularly ferrite-core loops
  surprisingly good sensitivity
  can rotate to find direction of a signal or to null out interference
  home construction possible
Tuned loop disadvantages:
  single frequency tuning
  is sensitive to local electrical noise in nearby residential wiring

## Slide 17: Antenna Alternatives -- bidirectional
Broadband loop antennas

## Slide 18: Antenna Alternatives -- bidirectional
Broadband loop
advantages:
  wideband response
  inexpensive home construction is possible
  can be mounted near the ground, and draped over foliage
  can be positioned to null interference
  can be placed away from noise sources
  relatively insensitive to local noise
disadvantages:
  low signal output, often requires preamplifier
  need to be aware of nulls when placing antenna

## Slide 19: Antenna Alternatives -- unidirectional
unidirectional antennas
--choices?
Narrow lobe in just one direction

## Slide 20: Antenna Alternatives -- unidirectional
unidirectional antennas
--choices?
Narrow lobe in just one direction
Broad front lobe, broad rear null

## Slide 21: Antenna Alternatives -- unidirectional
unidirectional antennas
--choices?
Narrow lobe in just one direction
Broad front lobe, broad rear null
Sharp null in one direction, broad lobe in other
At least one of the above criteria can be provided by a family of unidirectional antennas, the “non-resonant terminated loop”

## Slide 22: Antenna Alternatives -- unidirectional
non-resonant terminated loops:
  Ewe
  K9AY
  Flag
  Kaz / terminated delta
  Conti “superloop”
---these are mostly refinements of Earl Cunningham’s Pennant antenna derived from Floyd Koontz’ Ewe antenna
Notes: )

## Slide 23: Antenna Alternatives -- unidirectional
non-resonant terminated loops
  fit in a city lot, though can be somewhat larger
  are terminated with approximately 1kΩ resistance opposite the signal take-off point
  termination faces towards direction of null
  termination can be variable and remotely controllable
  signal take-off is via transformer or preamplifier
  are broadbanded

## Slide 24: The “Ewe”
Antenna Alternatives -- unidirectional

## Slide 25: Antenna Alternatives -- unidirectional
Ewe
advantages:
  strongest signal output for its size of all the unidirectional antennas
  simple construction for the homebrewer
disadvantages:
  requires two vertical supports and two ground rods
  needs a good ground

## Slide 26: The K9AY
Antenna Alternatives -- unidirectional

## Slide 27: Antenna Alternatives -- unidirectional
K9AY
advantages:
  single vertical support
  small footprint
  can be homebrewed
  a crossed pair can provide a multi-directional array
  array is commercially available
disadvantages
  needs a good ground or multiple radials
  likely needs a preamplifier for MW
  array is fairly complex if home built

## Slide 28: The Flag
Antenna Alternatives -- unidirectional

## Slide 29: Antenna Alternatives -- unidirectional
Flag
advantages:
  better signal output compared with a delta with the same linear footprint
  fairly easily homebrewed
  no grounding required
disadvantages
  two vertical supports
  termination and output feedline are halfway up the vertical elements

## Slide 30: The “Kaz” / terminated delta
Antenna Alternatives -- unidirectional

## Slide 31: Antenna Alternatives -- unidirectional
Kaz /terminated delta
advantages:
  single vertical support
  no grounding required
  easily scaled up or down
  easily homebrewed
  easily assembled and taken down
disadvantage:
  slightly lower output signal for same footprint compared with Flag or Ewe

## Slide 32: The Conti “Superloop”
Antenna Alternatives -- unidirectional

## Slide 33: Antenna Alternatives -- unidirectional
Conti “Superloop”
advantages:
  not ground dependent
  easily scaled up or down
  easily homebrewed
  fairly easily assembled and taken down
  signal output higher than a delta with the same linear footprint
disadvantages:
  slightly lower output signal for same footprint compared with Ewe
  two vertical supports required

## Slide 34: Antenna Alternatives -- really?
Is a non-resonant terminated loop an alternative to a DKaz?
All non-resonant terminated loops give much the same depth of nulls to stations off the back end of the antenna.
  These nulls are in the range of 10-25dB, sometimes even deeper, depending on termination resistance and depending on how far skewed away is the null from directly off the back of the loop
Also, signal strengths off the front end of these loops are within a couple of dB of what a DKaz can deliver.
So, how good are they compared to a DKaz?

## Slide 35: Antenna Alternatives -- really?
Is a non-resonant terminated loop an alternative to a DKaz?
DKaz
Flag
But....can a little Flag go head-to-head with a big DKaz?
The DKaz is a gold standard DX antenna...
(or is it an unfair contest?)

## Slide 36: Antenna Alternatives -- really?
A standard sized Flag antenna was compared with a 160 foot long DKaz at Grayland, WA, both aimed at 270 degrees
The DKaz signal is heard first in the following NetSDR playback, followed by the Flag’s
Listen to and watch for the difference on 4RN-792.

## Slide 37
Antenna Alternatives -- really?

## Slide 38: Antenna Alternatives -- really?
We should really care most about the “carrier to noise” ratio.

## Slide 39: Antenna Alternatives -- really?
If the signal strength is averaged for 25 seconds either side of the changeover point from DKaz to Flag for both carrier and for noise in the recorded NetSDR file, the following relationships are found:
 | Carrier 792.002kHz | Noise 793.000kHz | C/N ratio
Flag average signal strength | -92.0 dBm | -132.1dBm | 40.1 dB
DKaz average signal strength | -94.5 dBm | -139.2dBm | 44.7dB
So the DKaz has 4.6 dB better C/N than Flag, at least for 4RN-792
Note that the Flag’s absolute strength on 792 is actually slightly better than the Dkaz’

## Slide 40: Antenna Alternatives -- really?
If we look at example horizontal patterns generated by EZNEC antenna modeling software, we can see subtle differences in response off the back ends of the Flag and of the 160’ DKaz
Flag
DKaz
Straightforward front to back ratio looks similar, but the DKaz has generally less response, especially over the back facing 180 degree slice.
Is there a way to quantify this relationship in clearer terms than front to back ratio?

## Slide 41: Antenna Alternatives -- really?
In the radio amateur world, Receiving Directivity Factor (RDF) is often used as such a measure:
RDF is an arbitrary number that can be defined as the ratio in the average signal level delivered by the antenna over +/-10 degrees from the point of maximum response both in altitude and in azimuth compared with the average signal delivered by the antenna from every direction.

## Slide 42: Antenna Alternatives -- really?
EZNEC allows us to calculate RDF for a given antenna when a 3D pattern is calculated
The Flag has an RDF of 7.8dB
The DKaz has an RDF of 9.6dB
---an advantage of 1.8dB to the DKaz
This <2dB in an expression of antenna “goodness” doesn’t seem like much, but a couple of dB can make the difference between hearing DX and not hearing it in rough conditions.

## Slide 43: Antenna Alternatives -- really?
We observed that the DKaz had 4.6 dB better C/N than Flag, not 1.8dB
RDF is arbitrary. There is at least one other measure of antenna “goodness”
A coastal DXer will often be happy to accept any signal arriving from overseas, so a derivation known as Directivity Merit Figure (DMF) may be preferable.
DMF compares an antenna’s average forward response in that +/-10degree “sweet spot” to the average signal response of the antenna to the half hemisphere of noise and interference that a coastal DXer would want to reject. In other words....

## Slide 44: Antenna Alternatives -- really?
We observed that the DKaz had 4.6 dB better C/N than Flag, not 1.8dB
RDF is arbitrary. There is at least one other measure of antenna “goodness”
A coastal DXer will often be happy to accept any signal arriving from overseas, so a derivation known as Directivity Merit Figure (DMF) may be preferable.
DMF compares an antenna’s average forward response in that +/-10degree “sweet spot” to the average signal response of the antenna to the half hemisphere of noise and interference that a coastal DXer would want to reject. In other words,
The response from here:

## Slide 45: Antenna Alternatives -- really?
We observed that the DKaz had 4.6 dB better C/N than Flag, not 1.8dB
RDF is arbitrary. There is at least one other measure of antenna “goodness”
A coastal DXer will often be happy to accept any signal arriving from overseas, so a derivation known as Directivity Merit Figure (DMF) may be preferable.
DMF compares an antenna’s average forward response in that +/-10degree “sweet spot” to the average signal response of the antenna to the half hemisphere of noise and interference that a coastal DXer would want to reject. In other words,
compared with just the response from here:
The response from here:

## Slide 46: Antenna Alternatives -- really?
A program called “LBDXview” calculates Directivity Merit Figure:
The Flag has a DMF of 12.9dB
The DKaz has a DMF of 19.3dB
---an advantage of 6.4dB to the DKaz, a little closer to the 4.6dB C/N that was observed on 4RN

## Slide 47: Antenna Alternatives -- really?
DMF is also arbitrary, of course....but I think we can safely say...

## Slide 48: Antenna Alternatives -- really?
DMF is also arbitrary, of course....but I think we can safely say...
There is no alternative
to the DKaz, at least for the DXpeditioner.
On the other hand, the non-resonant terminated loops such as the Flag or Superloop, are ideal for the space limited DXer